Guide Specification - SECTION 08 51 13  ALUMINUM WINDOWS

ADA ACCESSIBILITY SUPPLEMENT

WAUSAU INventTM Family or 4250-Z Zero Sightline Series Projected and Casement

[NOTE: Instructional and advisory language in grey or blue italic font.]

[NOTE: Supplemental accessibility language in bold blue font.]

PART 1 GENERAL

  - SUMMARY

  - REFERENCES

1.03 SYSTEM DESCRIPTION AND PERFORMANCE REQUIREMENTS

- Design Wind Loads

- Air, Water and Structural Performance Requirements

- Life Cycle Testing

- Condensation Resistance and Thermal Transmittance Performance Requirements

- Acoustic Performance Requirements

- Sustainable Design Requirements

- Accessibility: As indicated on architectural drawings, one operable window in each occupied space shall meet the operating force limits and motion restrictions of ICC/ANSI A117.1 Section 309.4, when tested in an AAMA-accredited laboratory in accordance with AAMA 513.

1.  No reductions or allowances in laboratory-tested air, water or structural performance shall be acceptable for accessible operating vents.

2. Accessible hardware options may result in a more limited vent opening than non-accessible hardware packages.

[Specifier Note: Select hardware options that have been tested to comply with requirements of ICC/ANSI A117.1.  Roto-operators are required on project-out awning and casement vents. Also note that all code-required operable windows in a given occupied space may be required to meet these restrictions.]

  - SUBMITTALS

- General Requirements

- Shop Drawings

- Samples

- Test Reports and Calculations

  - Submit certified independent laboratory test reports from an AAMA-accredited test laboratory verifying compliance with all test requirements of 1.03, including confirmation of ADA accessibility per AAMA 513.

  - Submit structural calculations indicating adequacy of all materials furnished under this section, to meet the uniform and structural load requirements as specified in 1.03.

  - QUALITY ASSURANCE

  - DELIVERY, STORAGE AND HANDLING

  - WARRANTY

PART 2 PRODUCTS

2.01 MANUFACTURERS

2.02 MATERIALS

2.03 COMPONENTS

- Hardware (Select from options as noted)

  - All steel components including attachment fasteners to be stainless steel, except as noted.

  - Extruded aluminum components 6063-T5 or -T6.

  - Locking handles, bases and strikes to be die-cast, white bronze or stainless steel.

  - Thermo-plastic or thermo-set plastic caps, housings and other components to be injection-molded nylon, extruded PVC or other suitable compound.

  - Hardware to be occupant-operated, accessible, and include: (Select from appropriate options listed in the Wausau Hardware Selection Guide: stainless steel four-bar hinges, extruded aluminum butt hinges, linear operation keepers, single-handle Euro multi-lock, roto-operators, concealed friction adjusters and concealed limited opening devices.)

[Architects Note: Make sure operable windows and hardware are located and detailed in a way that meets the “reach” limitations of ICC/ANSI A117.1. Different height requirements apply to “obstructed” and “front” reach. There are also physical limits on clearances and protrusions, as well as approach area.]

2.04 FABRICATION

2.05 FINISHES

PART 3 EXECUTION

3.01 EXAMINATION

3.02 INSTALLATION

- Erection of Aluminum Windows

  - Install all windows with skilled workers in accordance with approved shop drawings, installation instructions, specifications and the “AAMA Commercial Window and Door Installation Manual.”

  - Vent windows must be installed -- and must remain -- plumb, square and level, to one-half of the unit shimming tolerances cited in the “AAMA Commercial Window and Door Installation Manual,” for proper weathering and operation.

  - Accessible operating vents will require additional care in installation, final adjustment and maintenance to achieve and maintain compliance.

  - Aluminum that is not organically coated shall be insulated from direct contact with steel, masonry, concrete or other dissimilar metals by bituminous paint, rust-inhibiting primer, non-conductive shims or other suitable insulating material.

DISCLAIMERS:

Wausau Window and Wall Systems takes no responsibility for product selection or application, including, but not limited to, compliance with building codes, safety codes, laws, merchantability or fitness for a particular purpose; and further disclaims all liability for the use, in whole or in part, of these Guide Specifications in preparation of project specifications and/or other documents. Guide Specifications are subject to change at any time, without notice, and at Wausau’s sole discretion.

With proper substrate conditions, installation, final adjustment and maintenance, those products proposed for use that are identified as accessible will meet ADA accessibility criteria per ICC/ANSI A117.1 Section 309.4 Operation, as demonstrated by testing in accordance with AAMA 513, with results subject to scope limitations and reductions cited therein, unless noted otherwise. Wausau Window and Wall Systems makes no claim, and takes no responsibility for; ADA compliance of the total window or door installation on site, including but not limited to, hardware, approach area, reach, force(s), motion, etc., nor for acceptance by authorities having jurisdiction. Wausau’s total representation of ADA operating forces and motions is defined herein. No further testing is included unless specifically noted.

“INvent” is a trademark of Apogee Wausau Group, Inc. All rights reserved. ©2014 Apogee Wausau Group, Inc.